## Slide 1: Electric Drive Vehicles for Mail Delivery: Identifying Key Issues
Michael Ravnitzky
May 14, 2009 Adv. Workshop in Regulation and Competition
CRRI – Rutgers University
28th Annual Eastern Conference
Notes: <number>

## Slide 2: Disclaimer
  The views expressed in this paper are those of the author and do not necessarily represent the opinions of the Postal Regulatory Commission.
Notes: <number>

## Slide 3: Summary
  Electric vehicles are well-suited to postal delivery.
  Deployment of an electric drive postal fleet would financially and structurally benefit both the Postal Service and national electrical grid operators.
  The obligation for broader use of renewable energy sources necessitates more energy storage capacity.
Notes: <number>

## Slide 4: 1895 – 1915: Electric Vehicle Dominance
  Most delivery trucks were electric
  Gasoline became cheap and convenient
  Development of intercity, rural roads
  WWI spurred ICE improvement and leftover trucks
Notes: <number>

## Slide 5: Postal Service Delivery Fleet
  Largest civilian fleet with 219,000 vehicles, including:
  142,000 Long Life Vehicles (LLVs)
  8,000 2-ton walk in trucks
  26,000 minivans
  21,000 Flexible Fuel Vehicles (FFVs)
  Many nearing end of vehicle rated lifespan
Notes: <number>

## Slide 6: Postal Fleet Attributes
Stop-and-start driving; low speed driving
Delivery to every home and business (“the last mile”)
Predictable, repetitive, limited length routes
Brief daily daytime usage cycle
Relatively low density lightweight loads
Varied weather and climate conditions
Notes: <number>

## Slide 7: EV’s Don’t Need:
pistons transmission engine oil
valves spark plugs starter
clutch exhaust pipes oil filter
fuel pump fuel filter air filter
water pump timing belt fan belt
muffler catalytic converter distributor
Notes: <number>

## Slide 8: Charging Infrastructure
Off-peak charging
Daily return to a fixed base
Centralized postal fleet reduces costs
Flexibility on vehicle charging voltage, power levels
May require local electric system upgrades
Notes: <number>

## Slide 9: Delivery Costs
Delivery - the largest single USPS cost component:
$23+ billion per year
Delivery vehicle maintenance and fuel costs:
$1.4 billion per year
1.8 million new delivery points are added each year.
Notes: <number>

## Slide 10: Reducing Delivery Costs
Drastically reduced fuel consumption
Reduced maintenance expense
Negotiated electricity purchase at off-peak rates
Lower overall life-cycle costs
High torque means more efficient route traverse
Notes: <number>

## Slide 11: Reducing Pollution
Removes mobile pollution and fuel cycle emissions
Replaced with point sources, scrubbers
High stacks in less inhabited areas
Less employee exposure to pollutants, particulates
Reduced pollution in residential areas and cities
Notes: <number>

## Slide 12: Reduced Risk of Technological Obsolescence
EV’s - less risk of technological obsolescence.
Power source and drive mechanism are distinct.
Electric vehicles can retrofit better batteries.
Notes: <number>

## Slide 13: Battery Requirements
Energy density (miles)
Power density (acceleration/braking)
Cycle lifespan (charge cycles)
Calendar lifespan (years)
Cost and there are others…
Notes: <number>

## Slide 14: Battery Selection
Lithium Iron Phosphate batteries
Reliability and Safety
Mass Manufacture
Environmental Issues
Notes: <number>

## Slide 15: Vehicle to Grid (V2G)
Provides ancillary services to wholesale markets
Increases stability of the electric grid
Permits greater use of variable renewable sources
Increases quality of electric power, reduces costs
Postal fleets can offer aggregated electric storage
Notes: <number>

## Slide 16: USPS Revenue Opportunity
Postal Service aggregation and sale of V2G services to ISOs/RTOs could bring in revenues of $2000-$2500 per vehicle per year.
Notes: <number>

## Slide 17: Advantages for RTOs/ISOs
Contingency (spinning) reserve
Ancillary service (regulation, balancing)
Overall grid stability – “islands of stability”
Increased competition in wholesale markets
Improved power quality, phase (R) control
Notes: <number>

## Slide 18: Renewable Source Quandary
State and Regulator mandates to add renewables
Wind power and solar power are erratic and variable
Adding renewables can lead to power ramping, drops
Requires either transmission lines or energy storage
Notes: <number>

## Slide 19: Regulation Services
The main benefit of V2G is regulation/ancillary services.
“Energy output is incidental to providing regulation.”
Output duration is shorter than typical tariff structure.
Tariff rules require adjustment for V2G characteristics.
Notes: <number>

## Slide 20: Tariffs to Encourage Energy Storage
NYISO Energy Storage Filing (March 11, 2009)
Proposed Tariff Revisions to Integrate Energy Storage Devices into NYISO-Administered Regulation Service
Batteries, Flywheels, etc.
Allows non-traditional resources (LESRs) to participate in the organized markets on fair terms.
Notes: <number>

## Slide 21: What’s needed?
Rigorous Cost Analysis of Postal EV Lifecycle
Comparison with Baseline USPS Fleet Strategy
Evaluation of Postal Service Routes for EV Suitability
Discussions between USPS and RTOs/ISOs
Notes: <number>

## Slide 22: What else is needed?
Implementation of Suitable Energy Storage Tariffs
Robust Common Interface/Communication Standards
Specifications for USPS Electric Delivery Truck
Government Involvement to Kickstart Procurement
Notes: <number>

## Slide 23: Conclusions
  Electric vehicles are well-suited to postal delivery.
  Deployment of an electric drive postal fleet would financially and structurally benefit both the Postal Service and national electrical grid operators.
  The obligation for broader use of renewable energy sources necessitates more energy storage capacity.
Notes: <number>

## Slide 24: Postscript
As a government agency performing a constitutionally-mandated critical public service, the Postal Service should be a first mover on electric vehicles, and be aided in that effort by the federal government.
Notes: <number>